## Slide 1: Implementation of SKINNY-AEAD Lightweight Cipher Course: ECE 592 / CSC 591: Cryptographic Engineering and Hardware Security
Presentation by:
Nikshipth Maddugaru - nmaddug
Shiraz Anwar Khan - skhan25

## Slide 2
Introduction
What is SKINNY-AEAD?
  SKINNY-AEAD is a family of lightweight “Authenticated Encryption with Associated Data” (AEAD) algorithms.
  Lightweight cryptographic algorithm designed for IoT and embedded systems.
Key Features:
  Encrypts fixed-size blocks of 128 bits (16 bytes).
  Supports key lengths of 128, 192, and 256 bits.
  Operates on a 4×44×4 matrix of bytes (state).

## Slide 3
Implementation Overview
Target Platform: Xilinx Spartan-7 FPGA.
  Design Strategy:
    Modular implementation of core operations: SubCells, AddConstants, AddRoundTweakey, ShiftRows, MixColumns.
    Optimized for resource efficiency and encryption speed.
  Flow Control States:
    IDLE → LOAD → SC → AC → ART → SR → MC → DONE.

## Slide 4
Numerical Comparison
Analysis:
Achieved significant area reduction and frequency improvement.
Trade-off in throughput due to optimizations prioritizing area efficiency.
Metric | Baseline | Proposed Design
Area (LUTs) | 7627 | 6194 (-18.8%)
Frequency (MHz) | 184 | 250 (+36%)
Throughput (Mbps) | 406 | 104.4 (-74%)

## Slide 5
Transition to Spartan-7 FPGA
Reasons for Switching:
  Cost efficiency for lightweight cryptography applications.
  Adequate resources for SKINNY-AEAD implementation.
  Lower power consumption compared to Kintex-7.
Implications:
  Maintained area and frequency optimizations on Spartan-7.
  Successfully adapted design without significant performance loss.

## Slide 6
Claimed Novelty
Innovations in Design:
  Efficient state transitions for optimal latency.
  Custom S-Box implementation using combinational logic to minimize lookup time.
Key Achievements:
  Balanced trade-offs between area efficiency and cryptographic performance.
  Demonstrated suitability for resource-constrained environments.

## Slide 7
Conclusion
Successfully implemented SKINNY-128-384 on Xilinx Spartan-7 FPGA.
Achieved balance between area efficiency and performance for lightweight cryptography.
Future Work
Explore parallel processing for higher throughput.
Support flexible block sizes for enhanced versatility.

## Slide 8
References
C. Beierle, J. Jean, S. Kölbl, G. Leander, A. Moradi, T. Peyrin, Y. Sasaki, P. Sasdrich, and S. M. Sim, “Skinny-AEAD and Skinny-Hash,” IACR Transactions on Symmetric Cryptology, vol. 2020, Special Issue 1, pp. 88–131, 2020. [Online]. Available: https://tosc.iacr.org/index.php/ToSC/article/view/8619
C. Beierle, A. Bogdanov, G. Cassagne, T. Fuhr, E. Lallemand, F.-X. Standaert, and G. Leurent, “SKINNY: A Lightweight Block Cipher for Low-Resource Devices,” Cryptology ePrint Archive, Paper 2016/660, 2016. [Online]. Available: https://eprint.iacr.org/2016/660
D. A. Wagner and J. Kelsey, “Tweakable Block Ciphers,” 2002, accessed: Dec. 7, 2024. [Online]. Available: https://people.eecs.berkeley.edu/daw/papers/tweak-crypto02.pdf
ChatGPT, “Assistance with FPGA Design and Cryptography Concepts,” OpenAI, 2024. [Online]. Available: https://openai.com/chatgpt